## Slide 1: Development of Analysis Techniques for Dynamic Magnetic Resonance Imaging of the Knee
Master Thesis Defense
Medical Photonics
Application to Tibiofemoral Kinematics
Jena | 25.10.2024 | Aayush Nepal | 198683 | Sumbitted on June 11, 2024

## Slide 2: Motivation: Relevance of knee kinematics
Knee osteoarthritis (OA) affects 10% men and 13% of women aged 60 and older (Zhang et al., 2010)
Altered tibiofemoral kinematics in OA patients can potentially accelerate disease progression (Farrokhi et al., 2014)
Even in ACL-deficient knees without instability symptoms, knee kinematics are altered (Yang et al., 2018)
Understanding tibiofemoral kinematics is key to assessing knee joint function
Jena | 25.10.2024 | Aayush Nepal

## Slide 3: Tibiofemoral kinematics
(Credit: Gray’s Anatomy 42nd ed.)
Six Degrees of freedom
3 Rotations
Flexion-Extension
Medial-Lateral
Abduction-Adduction
3 Translations
Anterior-Posterior
Meidal-Lateral
Compression-Distraction
Jena | 25.10.2024 | Aayush Nepal
Notes: If we can quantify any one of these motions accurately, then vital information might be revealed.

## Slide 4: The Setup
Jena | 25.10.2024 | Aayush Nepal
Notes: This device was developed (a few years ago) in collaboration with our partners at Charite Berlin

## Slide 5: Knee flexion-extension device
Jena | 25.10.2024 | Aayush Nepal
Repeated active open-chain knee flexion-extension exercise
5 volunteers
Guided by the beat of a metronome at 60 bpm
Once without additional weight and once with 12 kgs
Each scan lasted a duration of 160 seconds
Range of motion achieved within the scanner ~(30-46)°
Notes: This device was developed (a few years ago) in collaboration with our partners at Charite Berlin

## Slide 6: Imaging sequence and acquisition
Jena | 25.10.2024 | Aayush Nepal
Imaging the moving knee: Not your typical MRI setup.
Generally, we want to avoid movement inside the scanner.
A few different things allow us to overcome this challenge:
Lavdas 2012, doi:10.1016/j.mri.2012.04.001

## Slide 7: Imaging sequence and acquisition
Jena | 25.10.2024 | Aayush Nepal
Imaging the moving knee: Not your typical MRI setup.
Generally, we want to avoid movement inside the scanner.
A few different things allow us to overcome this challenge:
  Non-cartesian sampling of k-space: Radial Golden-Angle
  Speed!: Gradient Echo FLASH: Small flip angle allows for shorter repetition times
  Syncing and CINE:
    Each k-space contains data across a range of flexion angles
    Optical fibre position sensor samples the knee flexion precisely (0.0025°)
    Scanner data is synchronized with optical sensor data using trigger signals
    K-space data is sorted into 2-degree knee angle intervals
    A ‚cinema‘ or ‚movie‘ of the knee motion is created

## Slide 8: Reconstructed frames

## Slide 9: Methods: Edge Detection
Low Threshold: lower values are discarded (not an edge)
High Threshold: values higher are ‘Strong Edges’
In Between: ‘Weak Edges’ Only kept if connected to a strong edge
Hystereses Thresholding (Pixels and their gradient magnitude)
Strength of gaussian blur

## Slide 10: Methods: Edge Detection
Jena | 25.10.2024 | Aayush Nepal

## Slide 11: Methods: Connected Component Labelling
Jena | 25.10.2024 | Aayush Nepal
Skeletonization
Remove small objects
+
+
Treated the series of 2d arrays as a 3d volume.
3 × 3 × 3 structuring element
26-way connectivity

## Slide 12: Methods: Example sets
Jena | 25.10.2024 | Aayush Nepal
?
SET R
SET Q

## Slide 13: Methods: Issues with raw coordinates
Jena | 25.10.2024 | Aayush Nepal
?
SET R
SET Q
Lack of correspondance
Order matters
Inconsistent sampling
Uneven number of points
Inefficient computation

## Slide 14: Methods: Sorting and Downsampling
Jena | 25.10.2024 | Aayush Nepal
Sorting:
most distal and posterior point for the tibia, most proximal for the femur
nearest neighbor approach to create an ordered path
2. Cubic Spline Interpolation:
create a smooth, continuous curve that passes through all points in ordered set R
parameterize the curve using arc length
3. Downsampling and point placement
Equal interval = total arc length of spline / desired number of points
place points along the spline at these equal arc length intervals
SET R SET P

## Slide 15: Methods: Alignment of Set P to Q
Jena | 25.10.2024 | Aayush Nepal
?
SET Q
SET P

## Slide 16: Methods: Rigid Transformation for Edge Tracking
Jena | 25.10.2024 | Aayush Nepal
Set P
Set Q
A point in set P (x,y) undergoes the following transformation:
where, R(ϕ) is the 2D rotation matrix:
And (Δx,Δy) are the translations in the sagittal plane.
Optimize for: (Δx,Δy, )
2. A cost function that quantifies the misalignment between each (, y) and its nearest neighbour in set Q.

## Slide 17: Methods: Rigid Transformation for Edge Tracking
Jena | 25.10.2024 | Aayush Nepal
Set P
Set Q
Set P‘
Frame-by-frame transformation. Each transformed frame is used as reference for the next.
Nelder-Mead simplex algorithm („fmin search“)
Parameters:
Initial guess: [0,0,0]
Maximum iterations: 1000
Function tolerance and parameter tolerance: 1e-8
Once the set of parameters are obtained, any shape drawn on one frame on the bone will automatically be transformed to the rest of the frames

## Slide 18: Methods: Applying transformation
Jena | 25.10.2024 | Aayush Nepal

## Slide 19: Parameter extraction and tracking
Jena | 25.10.2024 | Aayush Nepal
Distance measurement
Angle measurement

## Slide 20: Calculations
Jena | 25.10.2024 | Aayush Nepal
Principle Component Analysis (PCA) was used to estimate the long axis of the bone segments.
- PCA identifies the direction of max. Variance
Simple euclidean distance formula was used for distance between the points
The time-axis had to be normalized due to varying ranges of motion of the subject‘s knee flexion angles.

## Slide 21: Results
Jena | 25.10.2024 | Aayush Nepal

## Slide 22: Conclusion and Outlook
Jena | 25.10.2024 | Aayush Nepal
No significant differences were found in the angle measurements between loaded and unloaded measurements
There was a significant differnce (P<0.016) in the flexion percentage range of 0-25%
Normative trends can be established with more healthy volunteers
Same volunteers should be re-measured to assess self-consistency
Patella can be tracked in a similar manner to extract patellofemoral kinematics too
A multi-slice approach could be adapted for 3d datasets for a more comprehensive 3d kinematic analysis

## Slide 23
Thank you for your attention!
Jena | 25.10.2024 | Aayush Nepal

## Slide 24: Supplementary materials
Jena | 25.10.2024 | Aayush Nepal

## Slide 25
Jena | 25.10.2024 | Aayush Nepal
Supplementary materials

## Slide 26: Supplementary materials
Jena | 25.10.2024 | Aayush Nepal